## Slide 1: Fall Update 3
Dev Bhatia
Ultrafast Optics Laboratory
Boston University

## Slide 2: Open Pipette Method for ADTR Measurement [1]
Rapid temperature measurement technique at the micron scale
  Carried out by using a microamp current amplifier
Synchronized laser irradiation would cause a local temperature change
  This would induce a resistance variation in the pipette
The measured pipette resistance was calibrated as a function of the ADTR
Fig 1. Open Pipette Method & The Geometric Relationship

## Slide 3: Theoretical Calculation of the ADTR [1]
Eq. 1 –
Mathematical Model of Heat Conduction Equation
Eq. 2 –
Equation 1 solved using a Gaussian approximation. ΔT obtained in consideration of the thermal lens effect
The thermal lens effect occurs when the laser beam is absorbed in the focusing region
Equation 2 predicted a linear relationship between the laser power and ΔT.
This deduction was confirmed via an open pipette method to measure the ΔT directly
  980-nm wavelength infrared laser irradiation

## Slide 4: Variable Considerations [1]
μa = 73.9 cm^-1 Optical Absorption Coefficient
R = 93.41 μm Beam waist at axial distance
z = 164.56 μm Axial Distance
tc = .01523 s Characteristic time of the thermal lens
P = .009999 W Irradiation laser power, obeys Beer-Lambert law with the initial laser power Po
κ = 0.6 W/mK thermal conductivity
ρ = 1000 kg/m^3 density of water
c = 4188 J kg^-1 K^-1 heat capacity
r = 25 μm radius of the fiber core
ρ = resistivity determined by the open pipette
γ = conductance of pipette
T = temperature
γo = solution conductance at To
αT = temperature coefficient of solution conductance

## Slide 5: Computed Values
Parameter | Calculated Value
Power at the Sample Plane | 2.9mW or 5.5mW
Beam Radius at the Sample Plane | 25.18 um
Beam Radius at the Waist | 25 um
Sample Plane Position (z-distance) | 117.55um
Characteristic Thermal Time Constant | 110.54um

## Slide 6: Implementation Strategy - Declarations
Important Considerations:
Array P0 contains initial power values
  Will be turned into irradiation laser power
Laser fiber is perpendicular to the axon
Laser is perfectly columnated
Fig 2.
Variable Declaration in Python

## Slide 7: Implementation Strategy – Integration & Loop
Fig. 3 – Computation of Temperature delta with variable Power

## Slide 8: Equation Implementation Results
A
B
C
D
E
Fig. 4 – Graphical Depiction of ΔT with respect to laser power

## Slide 9: Experimental Temperature Data
Fig 5. Complete Temperature Depiction using Matlab

## Slide 10: Comparison to Temperature Data
Fig. 6 – Peak temperature delta at independent times (a), experimental temperature transient (b)
a
b

## Slide 11: Conclusions
Shown previously is the peak temperature delta at independent times
  Different metric to the experimental data – shown in Fig. 5
Slope of the lower time regimes demonstrates a slower increase in temperature
  May be a symptom of the equation being used for modeling
Less Stabilization at higher regimes
Fig. 7 – Representative temperature transient

## Slide 12: Next Steps
Fix the Pulse Width, explore the creation of a temperature transient
Alter other variables, see how big of a role they play on modeling
Find alternative model equations that lead a more accurate result
  If the first bullet point is successful, this may not be needed

## Slide 13: Temperature Transient - Power
Fig. 8

## Slide 14: Temperature Transient – Z Distance
Fig. 9

## Slide 15: Temperature Transient – Optical Absorption Coefficient
Fig. 10

## Slide 16: Optical Absorption Coefficient
Figure 11 –
Specific absorption coefficient of water (725-2500nm) linearly interpolated from original data with a resolution of 5nm

## Slide 17: General Conclusions
Altering base parameters (z-distance, power, optical absorbtion) did not fix the issues with steepness/plateauing
  Certain combinations may yield promising results – combinations of higher z-distances with higher powers could change the model
It may be time to explore alternative models

## Slide 18: Temperature Transient – Power with Experimental
Fig. 12

## Slide 19: Temperature Transient – OAC with Experimental
Fig. 13

## Slide 20: Sources
K.F. Palmer and D. Williams, Optical Properties of water in the near infrared, Journal of the Optical Society of America, V.64, pp. 1107-1110, August, 1974
Zhu, Xuedong, Jen-Wei Lin, and Michelle Y Sander. "Infrared Inhibition and Waveform Modulation of Action Potentials in the Crayfish Motor Axon." Biomedical Optics Express 10, no. 12 (2019): 6580-6594.
Li, Xinyu, Jia Liu, Shanshan Liang, and Changsen Sun. "980-nm Infrared Laser Modulation of Sodium Channel Kinetics in a Neuron Cell Linearly Mediated by Photothermal Effect." Journal of Biomedical Optics 19, no. 10 (2014): 105002-105002.